## Slide 1
Lowest point
X m
X m NAP
Existing profile
Scenario 1
vertical_vertical_distance_type = ‘distance’
If X is negative  The bottom of the profile is flattened over a certain section/width of Y meters and than set to a level that is X meters below the current lowest point. The entire section deepened.
If X is positive  The bottom of the profile is flattened over a certain section/width of Y meters and than set to a level that is X meters above the current lowest point.
If the section currently lies entirely below this level, the entire section is raised. Otherwise, the section is only partly raised and other parts (that used to be higher) are deepened such that they have the same height.
Scenario 2
vertical_vertical_distance_type = ‘referencelevel’
IF X is lower than current lowest point  The bottom of the profile is flattened over a certain section/width of Y meters and than set to a reference height of X meters vs. a vertical datum (e.g. m NAP).
If the section currently lies entirely above this level, the entire section is deepened. If the section currently lies entirely below this level, the entire section is raised. Otherwise, parts of the section are raised (points that used to be lower than the reference height) and other parts are deepened (points that used to be higher than the reference height)
X m
Y m
Y m
Y m
X m NAP
Y m
Scenario 3
vertical_vertical_distance_type = ‘uniform’
If X is negative  The bottom of the profile is evenly deepened with a distance of X meters over a certain section/width of Y meters
If X is positive  The bottom of the profile is evenly raised with a distance of X meters over a certain section/width of Y meters
Y m
X m
Y m
X m
Y m
X m
Y m
X m NAP